## Slide 1: Input/Output
IFM
  Two 3x8 pe arrays share same input
  8 * 10(number of rows in an input tile) = 80bit per cycle
WGT
  Each pe array has different WGT
  8 * 2 * 3(kernel size) = 48bit per cycle
OFM
  Each pe arrays produces output of different output channel.
  8 output from each pe array total 16 output
  32 * 8 * 2 = 512bit per cycle
  Total 16 cycles required for a tile operation

## Slide 2: Input/Output
Parser
  IFM/WGT data width in input buffer is 512bit.
  IFM/WGT data width to conv_acc module is 80/48bit
  512 bit cannot be divided evenly with 80/48bit
  IFM parser stores 5 512bit data to produce 32 80bit input ifm data
  WGT parser stores 3 512bit data to produce 32 48bit input ifm data
  Parser sent input request to input buffer to fill the parser buffer again before using all of data
512bit
Total 32
80bit ifm

## Slide 3: PE_FSM
IDLE
  Before the start signal & after the end of convolution
S1
  State for filling ofm and wgt buffer
  When buffers are full(3 values for each buffer) move to S2
S2
  State that convolution occurs
  After convolution for one input tile is done, move to S1 and fill the buffer for new input tile
Count
  Cnt1 counts column of input tile, 0~3 range is for S1, 4~18 range is for S2
  Cnt2 counts number of input tiles calculated. 8 input tiles produce 1 output tile
  Cnt3 counts number of ofm tile produced. Cnt2 increased by 1 means are 2 ofm tile for different channels are produced.

## Slide 4: PE_FSM
Ifm_read / wgt_read
  Ifm_read signal is high for every cycle of convolutional operation
  Wgt_read rises when convolution for one input tile is done and falls after 3 wgt columns are stored in wgt buffer. Basically 1 in S1, 0 in S2
P_valid signal
  Signal indicating that output of pe is valid and need to be accumulated. Rises when first 3 inputs are multiplied and accumulated.
Last_channel signal
  Indicating current ifm tile is in last input channel and need to take outputs from ping-pong buffer after operation for this tile is done.